## Slide 1
GPU turns on, CPU is off, RAM is disabled
GPU executes 1st stage bootloader from ROM
1st stage bootloader loads 2nd stage bootloader from SD (/bootcode.bin) into L2 cache
1st stage bootloader (ROM)
2nd stage bootloader is executed
Enables RAM
Loads GPU firmware (/start.elf)
GPU firmware is executed
Loads configuration (/config.txt) optionally
Loads kernel (/kernel8.img)
Loads kernel parameters (cmdline.txt) optionally
Starts ARM core 0
Kernel is started
2nd stage bootloader (bootcode.bin)
GPU firmware (start.elf)
Power on
1st stage bootloader checks boot mode (for now only follow SD boot)
Raspberry Pi 3

## Slide 2
GPU turns on, CPU is off, RAM is disabled
GPU executes 1st stage bootloader from ROM
1st stage bootloader loads 2nd stage bootloader from SPI Flash into L2 cache
1st stage bootloader (ROM)
2nd stage bootloader is executed
Enables RAM
Loads GPU firmware (/start.elf)
GPU firmware is executed
Loads configuration (/config.txt) optionally
Loads kernel (/kernel8-rpi4.img)
Loads kernel parameters (cmdline.txt) optionally
Starts ARM core 0
Kernel is started
2nd stage bootloader (SPI Flash)
GPU firmware (start.elf)
Power on
1st stage bootloader checks boot mode (for now only follow SD boot)
Raspberry Pi 4

## Slide 3
GPU turns on, CPU is off, RAM is disabled
GPU executes 1st stage bootloader from ROM
1st stage bootloader loads 2nd stage bootloader from SPI Flash into L2 cache
1st stage bootloader (ROM)
2nd stage bootloader is executed
Enables RAM
Loads GPU firmware (/start.elf)
GPU firmware is executed
Loads configuration (/config.txt) optionally
Loads kernel (/kernel_2712.img)
Loads kernel parameters (cmdline.txt) optionally
Starts ARM core 0
Kernel is started
2nd stage bootloader (SPI Flash)
GPU firmware (start.elf)
Power on
1st stage bootloader checks boot mode (for now only follow SD boot)
Raspberry Pi 5